## Slide 1: Epidemic Broadcast
Marco Pinna
Yuri Mazzuoli
Rambod Rahmani

## Slide 2: General scenario
N users dropped randomly on a floorplan
One of them produces a message, which should reach everyone as soon as possible
Communications are slotted
Every user has a transmission radius R
Each user relays the message once with probability p and stops
Two or more transmission to the same receiver during the same slot produce a collision (receiver will not be able to decode the message correctly)

## Slide 3: Overview
Broadcast time T
Coverage C
Number of collisions X
Broadcast radius R
Transmission probability p
Number of users N
Length of the side of the floorplan L
"Aspect ratio" of the floorplan a
Density of users per square metre d (function of N, L and a)
METRICS
PARAMETERS
L = 100 m
N = 100
a = 1
1 m – 19 m
0.1 – 0.9

## Slide 4: Modelling
Three possible states for each node: listening, transmitting, sleeping
Graph theory to model wireless networks
  Gain insight on the system
  Graph quantities (i.e. eccentricity) for lower or upper bounds
  Help with validation
Simplified models with known behaviour
  Single queue
  Star 1-to-5
  Star 5-to-1

## Slide 5: Omnet++ Simulator
INET Framework for networking models

## Slide 6
Simulator validation
Two fixed configuration for testing, with known average outcomes
Star 5-to-1
Single queue

## Slide 7: Simulation parameters
200 repetitions per configuration
3 RNGs (X coord, Y coord, Bernoullian variable)
X, Y uniformly distributed (0 m, 100 m)
Full swipe for p (0.1 to 0.9 with 0.1 steps) and for R (1 m to 19 m with one meter steps)
100 hosts

## Slide 8: Results: coverage
No significant differences for R < 7 m (poorly connected graph)
Coverage grows more and more rapidly as R grows from 1 m to ~13 m Then there are diminishing returns
The lower p, the better (fewer collisions)
Apparently caps at R = 19 m (further data needed for high values of p)
Sigmoidal trend? (more about this later)
Notes: Ricordarsi di dire che per R ->sqrt(2)*L il coverage deve tendere al 100% quindi anche per le linee con p alto deve salire prima o poi

## Slide 9: Results: collisions
Almost no collisions for R < 8 m (again: poorly connected graph)
Linear trend with respect to range for 11 < R < 20
The lower p, the better (fewer collisions)
Should be identically null for (all nodes reached in the first slot)
More data is needed
Notes: Ricordarsi di dire che per R ->sqrt(2)*L il coverage deve tendere al 100% quindi anche per le linee con p alto deve salire prima o poi

## Slide 10: Results: broadcast time
Inversely proportional to p (cfr. avg of geometric distribution)
Lower p means: - more attempts needed - fewer paths cut off in the graph due to fewer collisions
Shorter time for low R because of poor graph connectivity
T(R) peaks at R=13 m (as does eccentricity)
Notes: Ricordarsi di dire che per R ->sqrt(2)*L il coverage deve tendere al 100% quindi anche per le linee con p alto deve salire prima o poi

## Slide 11: KPIs and graph properties: coverage
Study of coverage for limit cases: 1) p → 0 and 2) p → 1
p → 0 implies no collisions. Coverage C0 tends to the "reach" of node 0
Sigmoidal trend with possible closed form:
p → 1 system becomes fully deterministic (it only depends on the topology of the graph)
Negative returns for certain values of R (collisions take over the increase in connectivity)
No closed form for coverage C1 (yet)
If found, a closed form for C might be

## Slide 12: KPIs and graph properties: duration
Broadcast time curves exhibit the same trend as the eccentricity
Time hops attempts max hops = avg_attempts =
Additional ~0.8 scaling factor due to
1) multiple paths of length (the fastest "wins")
2) collisions may cut off some paths

## Slide 13: Performance optimization
Trivial solution: make R so big that it covers the whole floorplan (not viable)
To maximize the coverage (at possible expense of broadcast time): high R, low p
To minimize broadcast time (at possible expense of not having total coverage): high p choice of R not as trivial: to be chosen such that it does not fall in the "red zone"